## Slide 1: Optimizing CNN performance using RISC-V Custom Instructions Set for Edge AI inference Applications
Aila tej rithvik- 244102401

## Slide 2: Architecture of Co-Processor
PE
PE
PE
PE
Address Calculation
Unit
+
+
+
Input Buffer
output data
Input data
Starting Address
Address out
Control unit

## Slide 3: Processing Element
.
Input Reg.
(8x3x4)
Filter Reg. (3x3x4)
MAC Tree

## Slide 4: Instruction sets
1. Load Weights/Filters ( bunching together multiple filters and multiple channels)
2. Convolution Instruction
( loading data + performing Convolution + adding channels + write back)
Load and Store operations are done on alternative Clock cycles / interleaved way.
Each PE handles a separate input channel
Each PE holds multiple filters and calculates output for one filter in one clock-cycle

## Slide 5: Image and Filter sizes
Input Image Size - 8x8 , 4 channels
Filter size - 3x3, 4 channels , 4 Filters
Output Image Size – 6x6, 4 channels
Clock cycles Required
Baseline Processor ~ 70,000
Custom Hardware ~ 600 - 700

## Slide 6: Future Work
More Channels in Parallel – less Store Operations
More Filters in Parallel – Less Load Operations
More Parallelism/ more PEs, more on chip memory, better the energy efficiency
(less Load-Store Operations from External Memory)
Use SRAM based cache blocks instead of Registers/Flipflops.
Other techniques like Layer Fusion ( with Max-pooling).
Clock – Gating Registers, Low power Filp-flops.

## Slide 7: Image and Filter sizes